## Slide 1
Analytical Modeling and Experimental Verification for Transient Thermal Stratification in Solar Water tank with and without withdrawal loads
Student’s name: Sarah O. Adnan
Supervised by: Prof. Dr. Karima E. Amori

## Slide 2
OBJECTIVES
Develop an analytical model to predict the change in thermal storage status.
Examine the significant physical parameters of the tank and its inlet configurations and profile.
Carry out field tests on the thermal stratification in cylindrical tank.
Employ the analytical solution on the hexahedral tank under different operating conditions.

## Slide 3
Problem Statement
Global energy transformation from conventional energy resources and renewable energy resources are take place worldwide. Solar energy is a promising source of renewable energies. The enrolling of renewable technologies results no or much less gases emissions than conventional fuels therefore (TES) and its applications play important rule in meeting clean energy demand, achieving goals in terms of energy saving and reduce co2 emissions (Boulaktout et al., 2021).

## Slide 4
In solar systems, specifically in the storage tank, thermal stratification takes place naturally; the cold water remains at the bottom of the tank separated from the hot water, which flows to the top.
Thermal stratification phenomenon occurs due to density difference between fluid layers i.e. fluid with less density flows upward while fluid of higher density remain at the tank bottom.
Thermal stratification phenomenon occurs in nature like lakes what is known as Thermocline.

## Slide 5
Thermal stratification in heat storage tank can be characterized by different parameters as thermocline thickness, Richardson number, charging and discharging efficiency, Peclet number, Reynolds number etc.
Thermal stratification is affected by aspect ratio of the tank, tank interior design, tank material, porous media etc.

## Slide 6
Previous studies
Bolonina etal. (2009),carried experimental tests on storage system provided with pipe stratifier. The stratifier is selected to be with low thermal conductivity to prevent longitudinal heat transfer. It is equipped with non-return valve to prevent reversed flow from the tank to the valve. The valve opens only when water temp. inside and outside the pipe are also similar, so the right water level is achieved.
Bouhal etal. (2017), carried out CFD simulation on the thermal stratification inside storage adiabatic vertical tank by using adiabatic flat plate to eliminate the effect of eddy currents. The study proven that the flat plates at middle-top and three plates are optimal. Group of indicators were studied such as temperatures, Richardson number and stratification number.

## Slide 7
Experimental setup
The system includes the following main equipment:
Thermal energy storage tank with baffles inside the tank to enhance thermal stratification and restrict mixing, (D=41.5cm and L=100cm), the tank capacity equal to 130 litre.
Two Flat Plate Solar Collectors FPSC.
Connecting tubes.
Valves to control withdrawal loads.
The tank was completely insulated with the connecting tubes.

## Slide 8
-Thermosiphon flow takes place during the operation.
-cold water leave storage tank then enters the solar collector.
-hot water leaves solar collector then enters at the top section of the tank
FIG.1 schematic diagram of experimental setup.

## Slide 9
Factors affecting the solar system
The performance of renewable energy system depends on several factors as energy that is extracted from solar radiation, ambient temperature and wind velocity affects the performance of the solar unit, higher wind velocity increases thermal losses and also the design of the systems affects the water heaters performance.

## Slide 10
Implemented experiments
The test was carried out during sunny conditions and partly cloudy conditions.
.
The experimental plane extended to cover the followings:
First, the experiments are carried out, with presence of natural circulation from collector without withdrawal loads.
Second, flow rate of natural circulation was measured experimentally.
Third, Thermal stratification inside the tank was measured without natural circulation and with no withdrawal loads.
Fourth, Tank thermal stratification is measured as well as collectors inlet and exit temperatures when the withdrawal load is activated.

## Slide 11
Governing equations
Evaluating tank temperature in solar hot water heater.
Applying the instantaneous heat balance principle on the absorber yields:
Qa =QLA+wcp(T2-T1) ………………… (1)
where
Qa=absorbed energy by absorber (W/m2)
QLA=heat loss from absorber (W/m2)
W=water mass flow rate in the absorber(kg/s)
Cp=water specific heat (J/kg.K)
T2=outlet temp. from the absorber (oC or K)
T1=inlet temp. to the absorber (oC or K)

## Slide 12
Assume there is no heat loss in the connecting pipes, so the instantaneous heat balance in the tank yields:
Wcp(T2-T1)=qLT+wT(dTm/dt) ……..(2)
where
wT=equivalent water in the tank
qLT=heat loss from tank
Tm=tank mean temp.
t=time
For the thermosyphon flow hT=hf
hT= thermosyphon head
hf=friction load

## Slide 13
Sub. Eq (2) in eq (1) to obtain
qA=qLA+qLT+wT(dTm/dt) ……………(3)
An approximation to the solar irradiation of the absorber cover can be made using a sine function,
G=Gm sin (w1 t) ……………(4)
where
G=solar radiation incident on the absorber cover (W/m2)
Gm=maximum solar radiation W/m2
w1 is considered such that G=Gm at solar noon
t is time in (hour)
The heat loss from the absorber is
qLA=UAAA(Tab-T∞) ………………(5)
And heat loss from the tank is expressed as :
qLA=UTAT(Tm-T∞) …………..(6)

## Slide 14
where
UA overall heat loss coefficient from absorber (W/m2)
UT overall heat loss coefficient from tank (W/m2.K)
Aa absorber overall area m2
AT tank surface area based on the mean of internal and external radius (m2)
Tab mean absorber temp. (oC)
T∞ ambient temp. (oC)
The absorbed energy by the absorber is evaluated as
Qa= α τ β AA Gm sinw1t …………….(7)

## Slide 15
Where
α absorbtsnce of the absorber
τ transmissivity of the glass cover
β ratio of aperture area to collector area
The total heat loss from the system is ql=qLA+qLT ………….(8)
Sub. Eq. (7) and eq (8) in eq (3) yields
α τ β AA Gm sinw1t= (UAAA+ UTAT)(Tm-T ∞)+ wT(dTm/dt) …………(9)
Assuming that Tab=Tm ……………(10)
Also the ambient temperature can be approximated by a sine function of the form :
T ∞=T0+TL sinw2t2 ………………….(11)

## Slide 16
Where
t2 time from midnight (hr)
W2 factor considered to transform time to rad.
T0 average day temperature (0C)
TL amplitude of temperature for the considered day
Substituting equation (11) in equation (9) for T∞ and re arranging to get :
wT(dTm/dt)+ (UAAA+ UTAT)(Tm)= α τ β AA Gm sinw1t+ (UAAA+ UTAT)(T0+TL sinw2t2) …………(12)
The differential equation (12) can be solved to evaluate tank temperature Tm .