## Slide 2
Heat transfer enhancement in a pipe filled with metal foam
By: Raad Mohammed Kathem
Supervised by :
Assist. Prof. Dr. Sajida Lafta

## Slide 3
Porous media denote a system include a rigid matrix with connected void
Fluid through voids may be single-phase flow or two-phase flow
The sources Porous media can be:
Man-made (macroscopic packed spheres or column ,stacks of fissures and wood).
Metal foam
What Is Porous Media?
Introduction
Literature
Modeling
Recommendations
Conclusions
Nature, brick, limestone, rye bread, human lunged.

## Slide 4
While metal foam has a high thermal conductivity, it raises the stationary thermal conductivity of the flow field.
Metal foam increases the area of heat transfer between solid and fluid phases significantly.
Fluid is mixed with an additional thermal conductive in the cell of metal foam.
What Is Porous Media?
Introduction
Recommendations

## Slide 5
The porous media enhances the heat transfer in different energy type like renewable power (geothermal, Wind and solar) and increase efficiency of heat exchanger with other applications.
Applications
Chemical engineering: storage and drying of fruit and grain, underground radioactive waste, etc.
Mechanical engineering : Fibrous and granular thermal insulation for pipeline and equipment’s, cooling of nuclear fuel debris , Lubrication of synovial joints in human body such hip and knee and gas bearing.
Introduction
Literature
Modeling
Recommendations
Conclusions
Result

## Slide 6
Applications
Automotive industrial machines like as the door sill was filled with metal foam to increase the stiffness and reinforce, electric car segment, train support
Introduction
Literature
Modeling
Recommendations
Conclusions
Result
Heat exchanger, Bio-medical applications

## Slide 7
Literature
Review
Modeling
Introduction
Literature Review
The review of previous studies on convection heat transfer from 2000 to 2021.
The number of surveyed is about (45) which display in three sections:
Also, some of them used a heat exchanger, pipe , duct or two plates, and they were partially or completely filled with metal foam.
They are Notes the effect of different parameters such as porosity, pore density, the thickness of metal foam, GMF GPM , constant heat flux, constant wall temperature, and change in the geometry of the pipe.
Part of the research also be local thermal equilibrium and local thermal nonequilibrium
Recommendations
Conclusions
Result
A section of the research dealt with the theoretical side and the
other section dealt with the practical side
Most of the research investigated the pipe with metal foam numerically

## Slide 8
(Mancin et al. 2011,2012) studies the effect of the thickness of metal foam on heat transfer enhancement.
(Z.G. Xu et al. 2018) uses Gradient metal foams (GMFs) with different value of pore density (PPI) to study fully developed forced convective heat transfer in tubes filled partially with metal foam.
(Hamdi E. Ahmed et al. 2019) uses helical grooves

## Slide 9
(Prakash H. Jadhav et al. 2021, 2020) studied the influence thickness of metal from the center of the pipe to the wall with different values of (PPI)(10-45) and porosity (0.9-0.95).
(Liang Zhang et al. 2019) studied the influence of dimples on the surface of the pipe.

## Slide 10
Figure (1): Comparison of Numerical result of wall temperature between present study for the pipe filled with metal foam (10,40) PPI with prakash H.Jadhav et al. 2020.
Chart: q˝=275w/m² Re=1125 10PPI
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9
prakash H.Jadhav 2020 | 325 | 321 | 320 | 320 | 321 | 322 | 325 | 327 | 331
present work | 335 | 323.6 | 318.4 | 320.7 | 323 | 324.9 | 326.3 | 330.6 | 340
a) 10PPI, Re=1125
b) 10PPI, Re=3500
Chart: q˝=275w/m² Re=3500 10PPI
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9
Prakash H.Jadhav 2020 | 314 | 312 | 310 | 309.8 | 310.5 | 311 | 312 | 316 | 319
present work | 324 | 314.7 | 308.5 | 309.4 | 310.3 | 311.1 | 311.9 | 313.4 | 325
c) 40PPI, Re=1125
Chart: q˝=275 w/m Re=1125 40PPI
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9
Prakash H.Jadhav 2020 | 314 | 310 | 309 | 308 | 307.9 | 308 | 308.6 | 310.5 | 314
present work | 325 | 309.8 | 307.4 | 306.9 | 306.5 | 306.2 | 306 | 310.2 | 330
d) 40PPI, Re=3500
Chart: q̋ = 275W/m Re= 3500 40PPI
| 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9
Prakash H.Jadhav 2020 | 310 | 307 | 305.5 | 305 | 305.1 | 305.9 | 306.5 | 308 | 312
present work | 320 | 308.4 | 305.5 | 305.9 | 306.2 | 306.2 | 306.1 | 307.4 | 321
Validation
(a) 10PPI
Chart: q˝=275W/m² Model 2 10PPI
| 0.4 | 1 | 1.5 | 2 | 2.5 | 3
prakash H.Jadhav 2021 | 311 | 309 | 307 | 306.5 | 305.8 | 305.3
present work | 311.5 | 309.3 | 307.36 | 306.33 | 305.24 | 305
Chart: q˝=275W/m² Model 2 45PPI
| 0.4 | 1 | 1.5 | 2 | 2.5 | 3
prakash H.Jadhav 2021 | 307.5 | 306 | 304.5 | 304 | 303.6 | 303.5
present work | 306.8 | 305.1 | 304.1 | 303.87 | 303.5 | 303.3
(b) 45PPI
Figure (2) Comparison the results of a pipe partially filled with metal foam (10,45) PPI and the results of Prakash H. Jadhav in 2021.

## Slide 11
Objectives & Plan of The Work
The force convection heat transfer in a pipe with different cases was investigated
The aim of this research is to study numerically and experimentally the heat transfer enhancement inside a pipe subjected to constant heat flux filled partially or completely with metal foam and compared the result between them
Introduction
Literature
Modeling
Recommendations
Conclusions
Result

## Slide 12
l
M0deling
Modeling
Literature
Literature Review
Four parameter will be investigated
Geometry
Pore density
Heat
Flux
(″q)
Thickness
Numerical Simulation using Ansys Program
Experimental Work using different Test section
Compare the Experimental work with the Numerical simulation to verify the results
Scope of Present Work:
Recommendations
Conclusions
Introduction

## Slide 14
Modeling
Literature
Introduction
Scope of Present Work:
Experimental work

## Slide 15
40PPI
10PPI
Figure 2: Pore density of metal foam
Dimple pipe
Clear pipe
Figure 1: Test section of clear and dimple pipe

## Slide 16
1) Clear pipe
2) Case A
3) Case B
Axial-section dimple pipe
4) Case C

## Slide 17
6) Case E
7) Case F
5) Case D

## Slide 18
In the numerical part, it was used Ansys fluent program 2021 in different cases, the assumption
Three dimension model
the metal foam is isotropic, homogenous, uniform
constant thermophysical properties of the solid and fluid phases
The working fluid is a Newtonian and incompressible fluid and its flow is turbulent
Porosity 0.9 %, pore density (10,20,30, 40 PPI)
The numerical results are compared with data obtained from experimental work.

## Slide 19
Chart: Re Number
| 3261.4369999999999 | 6522.875 | 9784.3130000000001
Clear pipe | 47.8 | 53.7761 | 67.7
Numerical Case A, 10PPI | 139 | 155 | 179
Numerical Case A, 40PPI | 191 | 204 | 214
Experimental Case A, 10PPI | 137.9301 | 147.594 | 172.9284
Experimental Case A, 40PPI | 184.4522 | 197.3108 | 217.2993
Chart: Re Number
| 3261.4369999999999 | 6522.875 | 9784.3130000000001
Numerical Case B | 129.0631 | 194.3322 | 238.7072
Numerical Case C, 40PPI | 208.9891 | 229.688 | 245.705
Experimental Case B | 106.743 | 145.8247 | 230.874
Experimental Case C, 40PPI | 188.1649 | 210.8556 | 254.6865
Case A
Case B, C
Chart: Re Number
| 3261.4369999999999 | 6522.875 | 9784.3130000000001
Case D 10PPI | 187 | 238 | 265
Case D 20PPI | 224.832 | 270.736 | 292.939
Case D 30PPI | 247.923 | 285.954 | 302.8028
Case D 40PPI | 261 | 293 | 307
Case D
Chart: Re Number
| 3261.4369999999999 | 6522.875 | 9784.3130000000001
Case E 10PPI | 117.822 | 160.858 | 187.59
Case E 20PPI | 126.026 | 168.001 | 194.088
Case E 30PPI | 130.489 | 171.8287 | 197.5743
Case E 40PPI | 133.242 | 174.46 | 199.85
Case E
Chart: Re Number
| 3261.4369999999999 | 6522.875 | 9784.3130000000001
Case F 10PPI | 122.218 | 162.201 | 185
Case F 20PPI | 134.9489 | 173.903 | 197.1517
Case F 30PPI | 142.0603 | 178.8885 | 202.1924
Case F 40PPI | 148.226 | 183.17 | 205.53
Case F

## Slide 20
Case C
Chart: Re Number
| 3261.4369999999999 | 6522.875 | 9784.3130000000001
Numerical Case A, 10PPI | 2.9079 | 2.8823 | 2.644
Numerical Case A, 40PPI | 5.4603 | 5.4485
Experimental Case A, 10PPI | 2.7923 | 2.5865 | 2.5174
Experimental Case A, 40PPI | 3.7341 | 3.4577 | 3.1633
Case A
Chart: Re Number
| 3261.4369999999999 | 6522.875 | 9784.3130000000001
Numerical Case B | 2.7001 | 3.6137 | 3.526
Experimental Case B | 2.161 | 2.5555 | 3.3609
Case B
Chart: Re Number
| 3261.4369999999999 | 6522.875 | 9784.3130000000001
Numerical Case C, 40PPI | 3.9958 | 3.7935 | 3.161
Experimental Case C, 40PPI | 3.8093 | 3.6951 | 3.7076
Case D
Case E
Chart: Re Number
| 3261.4369999999999 | 6522.875 | 9784.3130000000001
Case D 10PPI | 3.9121 | 4.4258 | 3.9143
Case D 20PPI | 4.7036 | 5.0345 | 4.327
Case D 30PPI | 5.1867 | 5.3175 | 4.4727
Case D 40PPI | 5.4603 | 5.4485 | 4.5347
Chart: Re Number
| 3261.4369999999999 | 6522.875 | 9784.3130000000001
Case E 10PPI | 2.4649 | 2.9913 | 2.7709
Case E 20PPI | 2.6365 | 3.1241 | 2.8669
Case E 30PPI | 2.7299 | 3.1953 | 2.9184
Case E 40PPI | 2.7875 | 3.2442 | 2.952
Chart: Re Number
| 3261.4369999999999 | 6522.875 | 9784.3130000000001
Case F 10PPI | 2.5569 | 3.0162 | 2.7326
Case F 20PPI | 2.8232 | 3.2338 | 2.9121
Case F 30PPI | 2.972 | 3.3265 | 2.9866
Case F 40PPI | 3.101 | 3.4062 | 3.0359
Case F

## Slide 21
Chart: q″=31830.98 W/m²
| 3261.4369999999999 | 6522.875 | 9784.3130000000001
Case A, 10PPI | 637.2605 | 2442.788 | 5396.432
Case A, 40PPI | 2656.933 | 9877.469 | 21633.43
Case B | 20.03 | 63.49 | 125
Case C, 40PPI | 690 | 2770 | 6400
Clear pipe | 12 | 28.422 | 46.4688
Numerical result, case A, B,C
Chart: q″=31830.98 W/m²
| 3261.4369999999999 | 6522.875 | 9784.3130000000001
Case A, 10PPI | 500 | 1800 | 3500
Case A, 40PPI | 1800 | 6500 | 14000
Case B | 80 | 125 | 200
Case C, 40PPI | 1850 | 6600 | 15000
Clear pipe | 12 | 28.422 | 46.4688
Experimental result, case A,B,C
Chart: Re Number
| 3261.4369999999999 | 6522.875 | 9784.3130000000001
Case D 10PPI | 361.622 | 1361.97 | 2981.58
Case D 20PPI | 650 | 2440.647 | 5343.837
Case D 30PPI | 928.682 | 3442.572 | 7512.851
Case D 40PPI | 1200.25 | 4370.7141 | 9523.5954
Clear pipe | 12 | 28.422 | 46.4688
Chart: Re Number
| 3261.4369999999999 | 6522.875 | 9784.3130000000001
Case E 10PPI | 255.3 | 847.1495 | 1861.054
Case E 20PPI | 436.5626 | 1651.97 | 3633.932
Case E 30PPI | 660.786 | 2477.499 | 5437.092
Case E 40PPI | 896.85 | 3326.264 | 7274.9999
Clear pipe | 12 | 28.422 | 46.4688
Chart: Re Number
| 3261.4369999999999 | 6522.875 | 9784.3130000000001
Case F 10PPI | 326.7785 | 1245.72 | 2743.976
Case F 20PPI | 646.6659 | 2452.998 | 5403.393
Case F 30PPI | 983.018 | 3691.342 | 8108.229
Case F 40PPI | 1337.127 | 4964.51 | 10865.16
Clear pipe | 12 | 28.422 | 46.4688
Case D
Case E
Case F

## Slide 22
Clear pipe
Case B
Case D
Case F
Case E

## Slide 23
THANK You for Attention