## Slide 1
Tissue Fixation in Histology Preserving Cellular Structure for Microscopic Analysis
BY
Dr. Hadaf H. Mohammed

## Slide 2: Fixation in Histology
  Definition, principles, aims, properties, and major fixatives

## Slide 3: Definition of Fixation
  Complex chemical events preserving cell morphology
  Prevents autolysis and putrefaction
  Maintains structural detail

## Slide 4: Principle of Fixation
  Crosslinking of proteins
  Converts semifluid state to semisolid
  Maintains tissue architecture for manipulation

## Slide 5: Aims of Fixation
  Preserve tissue in normal state
  Prevent autolysis and putrefaction
  Preserve chemical components
  Hardening of soft tissues
  Optical differentiation

## Slide 6: Autolysis & Putrefaction
  Autolysis: enzymatic self‑digestion
  Putrefaction: bacterial breakdown producing gas

## Slide 7: Properties of Fixatives
  Coagulation and precipitation
  Penetration depends on molecular weight
  Fixative must be soluble in suitable solvent
  Concentration should be isotonic or hypotonic
  Most fixatives are acidic and must be neutralized

## Slide 8: Amount of Fixative
  Should be 15–20× tissue volume
  >50× for museum specimens
  Tissue slices should be 1.5 cm thick for penetration

## Slide 9: Formaldehyde (Formalin)
  37–40% w/v solution
  Cheap, rapid penetration, minimal over‑hardening
  Crosslinks proteins and denatures them
  Partially preserves glycogen
  Does not preserve neutral fats
  10% solution preferred

## Slide 10: Issues with Formalin
  Oxidizes to formic acid → pigment artifact
  Requires neutralization with calcium carbonate
  Prolonged exposure causes dermatitis and sinus irritation

## Slide 11: Alcohol Fixatives
  Ethyl alcohol commonly used
  Oxidizes to acetaldehyde → acetic acid
  Slow penetration, causes tissue shrinkage and hardening

## Slide 12: Osmic Acid (OsO₄)
  Excellent for fixation of lipids
  Slow penetration, expensive, toxic
  Used mainly for electron microscopy
  Stains lipids black

## Slide 13: Acetic Acid
  Good nuclear fixative
  Causes swelling of tissues (opposite of alcohol)
  Does not fix lipids
  Used in compound fixatives

## Slide 14: Mercuric Chloride
  Strong protein coagulant
  Good nuclear detail
  Tissues become very hard
  Leaves mercury pigment—requires removal

## Slide 15: Picric Acid
  Good for glycogen and soft tissues
  Improves staining with acid dyes
  Causes shrinkage if used alone
  Highly explosive when dry

## Slide 16: Compound Fixatives
  Combination of chemicals to enhance fixation quality
  Provide balanced nuclear and cytoplasmic fixation
  Include Bouin’s, Zenker’s, Carnoy’s fixatives

## Slide 17: Bouin’s Fixative
  Contains picric acid, formaldehyde, acetic acid
  Excellent for soft tissues and embryos
  Good for trichrome staining
  Causes yellow coloration—removed with ethanol

## Slide 18: Zenker’s Fixative
  Contains mercuric chloride and potassium dichromate
  Excellent nuclear fixation
  Not suitable for enzyme studies
  Leaves mercury pigment

## Slide 19: Carnoy’s Fixative
  Contains ethanol, chloroform, acetic acid
  Rapid fixation
  Excellent for chromosomes
  Causes marked shrinking

## Slide 20: Factors Affecting Fixation
  Temperature influences fixation speed
  Tissue size and thickness
  Type and concentration of fixative
  Duration of fixation

## Slide 21
  Fixation preserves structure and chemistry
  Choice of fixative depends on study type
  Proper fixation is essential for quality microscopy

## Slide 22
Fixative | Main Use | Advantages | Disadvantages
10% Neutral Buffered Formalin (NBF) | Routine histology, general tissue preservation | Good overall morphology, compatible with most stains, inexpensive, good penetration | Toxic, may mask antigens (affects IHC), slow fixation
Glutaraldehyde | Electron microscopy | Excellent ultrastructural preservation, strong protein cross-linking | Poor penetration, tissue over-hardening, expensive, toxic

## Slide 23
Fixative | Type | Main Use | Advantages | Disadvantages
Ethanol / Methanol | Coagulant | Cytology smears, rapid fixation | Rapid action, preserves nucleic acids, no cross-linking | Tissue shrinkage, brittle tissues
Carnoy’s Fixative | Coagulant | Chromosome studies, glycogen preservation | Very rapid fixation, good glycogen preservation | Tissue shrinkage, harsh on tissues
Bouin’s Solution | Compound fixative | Testis, GI tract, delicate tissues | Excellent nuclear & cytoplasmic detail | Picric acid hazard, yellow staining, poor for molecular studies
Osmium Tetroxide | Oxidizing fixative | Electron microscopy, lipid preservation | Excellent membrane & lipid preservation | Highly toxic, expensive, poor penetration
Zenker’s Fixative | Mercurial | Bone marrow, spleen | Good nuclear detail | Mercury toxicity, disposal problems