## Slide 1
Assist. Prof. Mustafa M. Al-Khatieeb
BDS, MSc (Ortho)
College of Dentistry, Baghdad University
Removable Thermoplastic retainers

## Slide 2
Thermoplastic
Denoting substances that become plastic on heating and harden on cooling, and are able to repeat these processes.

## Slide 3: Thermoplastic materials
The implementation of the biomaterials used for the fabrication of the clear aligner and retainers have led to a constant improvement in the performances of these appliances

## Slide 4: Thermoplastic materials: Which is better?
Polyester
Copolyester (of polyethylene terephthalate).
Polyethylene terephthalate modified with gycol (PETG).
Polycarbonate.
Thermoplastic polyurethanes.
Polypropylene.
are the dominant thermoplastic material mixtures used for the manufacture of clear aligners and invisible retainers

## Slide 6
Draw backs?

## Slide 7: Environmental factors
Temperature
Humidity
Salivary enzymes
Alteration of the polymer crystallinity elastic deformation might influence the properties, suggesting that the mechanical behaviour of dental thermoplastic materials varies due to environmental factors

## Slide 8
Clinical behavior of the thermoplastic materials is highly influenced by the thickness of the device

## Slide 9: Types of damage due to ageing ?

## Slide 10
in vitro ageing, including:
Adsorption of integuments
Microcrack
Abrasion at the cusp tips
Localized calcification

## Slide 11
The thermoforming process can affect on :
Physical and mechanical proprieties of various thermoplastic materials
Different thicknesses
Transparency
Water absorption
Surface hardness
Flexure and elastic moduli,
Tensile and flexural forces

## Slide 12
Pressure molding machine
Thermoforming Process
Vacuum thermoforming machine
?

## Slide 13
Vacuum thermoforming formers in the dental industry are used to imprint opposing bite and fabricate other dental appliances like sports mouth guards, bleach trays and orthodontic appliances. •These formers can use a variety of thermoplastics depending on necessary thickness and flexibility needed. •A vacuum former should be composed of a vacuum pump and a heating element Also known as thermoforming

## Slide 15: Pressure molding machine
Versatile pressure moulding machine for all applications in dental pressure moulding and orthodontics, equipped with scan technology and 6.0 bar working pressure, adjustable by pressure reducing valve on the unit. The unique thermally controlled infrared heater reaches working temperature in one second. All parameters such as temperature, heating and cooling times are programmed by reading the scanner or entering the corresponding code. The coloured 3.2" LCD display with a resolution of 320 x 240 pixel leads you through the single working steps of the pressure moulding process, providing further information on scanned material, its indication as well as a library with illustrated application hints for fabrication. Rear port for easy updates. Large model cup facilitates embedding of mounted models. Pellet container ensures optimum dispensing and storing of pellets.

## Slide 19
Model plate form
Stainless steel pellets

## Slide 20: Uses of thermoforming process

## Slide 24: The material can be divided in 3 main categories
Hard-elastic material:
eg: BIOCRYL® C (Hawley’s Retainer)
DURAN® (Splint therapy)
IMPRELON® (Custom trays, dressing carriers or bite plates)
2. Hard/soft compound material: eg: DURASOFT® pd
3. Soft-elastic material:
eg: BIOPLAST® (Soft splints, sports mouth guards and positioners or duplicate models)
BIOPLAST® bleach
COPYPLAST® Tougher (for bleach)
COPYPLAST® C Transparent and visco-elastic (retention splints)
BIOPLAST® XTREME (Sports mouth guards)

## Slide 31
Unbreakable, abrasion-resistant, transparent compound material with a hard and soft side. Hard side bonds to acrylic. Already pre-dried and vacuum-sealed for instant use.
Application
Minplast splints, bruxism splints, occlusal splints, intra-oral anti-snoring devices

## Slide 35: Clear fusion hybrid retainer

## Slide 36: ClearRetain Hybrid

## Slide 38: Q: What are the drawbacks of clear retainer? Q: What is the best gauge of clear retainer?

## Slide 47
Thanks for attention

## Slide 48: References
Indian dental academy
(J Bagh Coll Dentistry 2012;24(2):127- 136).
Raja et al. 2014
Bucci et al., 2019
Scheu dental company