## Slide 1: Various Implemented Applications of Mechatronics
Assist. Prof. Dr. Yarub Alazzawi
Al-Khwarizmi College of Engineering/ Mechatronics Engineering Dep.
https://scholar.google.com/citations?user=NhwcogoAAAAJ&hl=en

## Slide 2
Outline:
Proj-1: Self-Capacitance based Wireless Power Transfer for Wearable Electronics
Proj-2: A compact and energy-efficient ultrasound receiver using PTAT reference circuit
Proj-3: Multi-access In-vivo Biotelemetry using Sonomicrometry and M-scan Ultrasound
Imaging
Proj-4: Feasibility of Self-powering and Energy Harvesting using Cardiac Valvular
Perturbations
Proj-5: Design of CMOS telemetry circuits for in-vivo wireless sonomicrometry
Proj-8: Detection of Ventricular Catheter Occlusion by Monitoring the Intracranial Pressure
(ICP) using PVDF Piezoelectric Sensor
Proj-7: Feasibility of non-contact ultrasound generation using implanted metallic surfaces
as electromagnetic acoustic transducers
Proj-6: Self-powered system-on-chip for substrate computing and ultrasonic
communications
Proj-9: Ultrasound Harmonic Bio-sensing Using Floating-Gate PMOS Transistor
Proj-10: Bomb-sniffing locusts
Proj-11: Electronic tooth for wireless diabetes detection through saliva
Proj-12: AuNP Core-Shell Nanostructure for quantum-based biosensing
Proj-13: Contactless ultrasound communication and energy delivery for implantable devices
Proj-14: Smart mouthguard for pilot’s spin shrink estimation

## Slide 3: Proj-1:Self-Capacitance based Wireless Power Transfer for Wearable Electronics: Theory and Implementation
Yarub Alazzawi
PhD Thesis Defense
Advisor: Prof. Shantanu Chakrabartty
Adaptive Integrated Microsystems Laboratory (http://aimlab.seas.wustl.edu/)
Yarub alazzawi et.al, IEEE TBIOCAS 2019.

## Slide 4
Heart rate,
Respiratory rate
Smartwatch,
Fitbit
Insulin pump
Hearing aid
Smart shoes
Activity tracker
Internet
Gateway
Remote monitoring of wearable electronic devices
Wearable biomedical sensor
Andrea Aliverti,
Breathe 2017
Motivation: Wearables

## Slide 5: Motivation & Background
All these wearable and implantable electronics require energy source to be functional.
Tracking health wearable electronics
Meghan Rosen,
Science News 2016
Wireless human health monitoring
https://classifieds.justlanded.com/2018

## Slide 6: Challenge: Powering
Battery: Requires periodic charging
determines the size and weight of the wearable.
ROBIN WYLIE
arstechnica.com 2015
Energy capacity is limited by volume of the battery.

## Slide 7: Solution: Wireless Power Transfer (WPT)
Wireless Power Transfer
modalities
Radio Frequency (RF)
Induction
(Ind)
Ultrasound
(US)
Capacitive coupling
Some of these are remotely delivered, others are locally.
Salar Chamanian, et al., Sensors and Actuators 2016
Liu, Daerhan, et al., IEEE
TOPE (2018).
Roes, M. G. L., et al, Electronics Society. IEEE, 2011.
Wang, Edward J., et al. International Symposium on Wearable Computers. ACM, 2018.

## Slide 8: Self Capacitance-based WPT
Mouse
cadaver
External ground
Power
source
Floating
electrode
Energy
Harvester
(Receiver)
torso
tail
leg
arm
External ground
Power
source
Energy
harvester
Yarub alazzawi et.al, IEEE TBIOCAS 2019.

## Slide 9
Diagnostic Cage
Power
Source
Data
Monitoring
RF
Transceiver
Mouse Cadaver
Plexiglas
Plexiglas
Aluminum
Antenna-1
Antenna-2
Capacitive coupling setup
Power
Source
Experimental setup
Yarub alazzawi et.al, IEEE TBIOCAS 2019.

## Slide 10: PTE comparison
SC maximum efficiency degrades more gracefully with respect to
1
SC-based WPT demonstrates a superior PTE compared to the other WPT techniques
Self-capacitance (SC)

## Slide 11
PTE comparison
Maximum Efficiency for SC close to 100% even with millimeter size harvester form-factor
efficiency (%)
Self-capacitance (SC)
SC-based WPT demonstrates a superior PTE compared to the other WPT techniques,
SC-based WPT does not require any frequency adjustment when the transducer size or alignment changes.

## Slide 12
Induction
Tx coil
Ultrasound
Tx piezo
Self capacitance
Wearable
device
smart home
SC-WPB for multiple wearable devices
Power
Source
Different modalities of wireless power broadcasting (WPB)
Yarub alazzawi et.al, IEEE IOT 2020,

## Slide 13
External ground
Fringe fields
Power
Source
Body
1
Body
2
Body
n
Body
3
Displacement
current
torso
leg
arm
External
ground
Power
source
Equivalent circuit model for SC-WPB
Multiple objects (e.g. human bodies) complicate equivalent circuit model

## Slide 14
Ongoing work: SC-WPT for energy harvesters
Battery-less electronics
Electric charge propagation
Shoe power source
Wireless Charging from shoe power generator for self-powering

## Slide 15: Proj-2: A compact and energy-efficient ultrasound receiver using PTAT reference circuit
Conventional
sensing system
Preamplification and rectification units are removed.
Yarub alazzawi et.al,
ELSEVIER Microelectronics 2019.
Use reference as sensor frontend.

## Slide 16: PTAT: Reference Circuit
PTAT: Proportional To Absolute Temperature
Yarub alazzawi et.al,
ELSEVIER Microelectronics 2019.
PTAT resistance (R) can be used as an input port.
the subthreshold slope.
thermal voltage.
in room temp
the ratio of the sizes of transistors and .

## Slide 17: PTAT Current Sensing/Rectification
sub-threshold biasing:
Rectifier equation:
Yarub alazzawi et.al,
ELSEVIER Microelectronics 2019.

## Slide 18: Comparison with a conventional frontend
Yarub alazzawi et.al,
ELSEVIER Microelectronics 2019.
For the same sensitivity, TCA is more noisy and consumes more power, in addition to its nonlinearity and bigger size.
Property | Proposed (PTAT) | Conventional (TCA)
Circuit dimensions |  | 
Power dissipation |  | 
Circuit performance | linear | nonlinear
Input referred noise |  | 
Property | Proposed (PTAT) | Conventional (TCA)
Circuit dimensions |  | 
Power dissipation |  | 
Circuit performance | linear | nonlinear
Input referred noise |  | 

## Slide 19: Proj-3: Multi-access In-vivo Biotelemetry using Sonomicrometry and M-scan Ultrasound Imaging
Yarub alazzawi et.al, IEEE TBME 2017.

## Slide 20: Proj-4: Feasibility of Self-powering and Energy Harvesting using Cardiac Valvular Perturbations
Yarub alazzawi et.al, IEEE TBioCAS 2018.

## Slide 21: Proj-5: Design of CMOS telemetry circuits for in-vivo wireless sonomicrometry
The receiver is also designed using a pulse modulator which is configured to measure the energy of the ultrasonic pings received by the crystal.
Measured pulse-rates for different values of the input voltages and different values of the reference resistor (R).
The frequency of the generated pulses is proportional to the received energy and could be used to detect a received pulse.
Yarub alazzawi et.al, IEEE ISCAS 2016.

## Slide 22
smart structures
SSP
Microchip
Piezo
Central computer
Wireless sensor
Sensor node
Wireless signal
US Substrate Pulse Link
Smart Substrate Plate SSP
Structure health monitoring
Self-contained energy harvester
Bi-direction communication
Low-power embedded hardware
Yarub alazzawi et.al, IEEE MWCAS 2017.
Proj-6: Self-powered system-on-chip for substrate computing and ultrasonic communications

## Slide 23
Voltage
Regulator
Voltage
Multiplier
PZT
PZT
Receiver
Transmitter
PZT
Transceiver circuit implementation

## Slide 24: Proj-7: Feasibility of non-contact ultrasound generation using implanted metallic surfaces as electromagnetic acoustic transducers
we investigate the feasibility of using an in-vivo metallic implant like a stent for the generation of acoustic waves which can then be used for imaging areas inside or near the surface of the implant.
Yarub alazzawi et.al, IEEE BioCAS 2015.

## Slide 25: Proj-8: Detection of Ventricular Catheter Occlusion by Monitoring the Intracranial Pressure (ICP) using PVDF Piezoelectric Sensor
there is no published work or data about detecting the occlusion or the amount of it, and the discomfort of the patient is usually the sign doctors rely on to do the cleaning process

## Slide 26: Proj-10: Bomb-sniffing locusts
The signals in the bugs’ brains reflected those differences in vapor concentration

## Slide 27
Power
Source
RF
Transceiver
Data
monitoring
Rx
Tx
Human
Head
Phantom
Setup
Gel
phantom
Proj-11: Electronic tooth for wireless diabetes detection through saliva
An electronic tooth can be used to detect the amount of glucose inside the saliva

## Slide 28: Proj-14: Au-Silica-AuNP Core-Shell Nanostructure
500 nm
500 nm
AuNP
Silica-coated AuNP
Au
SiO2
Au
AuNP
Silica-coated AuNP
Au-Silica-AuNP Core-Shell
Quantum dots can be used to design implanted sensors for various applications

## Slide 29: Publications
Journals
Yarub Alazzawi, Kenji Aono, Erica L. Scheller , and Shantanu Chakrabartty. "Exploiting Self-capacitances for Wireless Power Transfer ." IEEE Transactions on Biomedical Engineering , 2019
Yarub Alazzawi, Oindrila Chatterjee, and Shantanu Chakrabartty. "A Compact and Energy-efﬁcient Ultrasound Receiver using PTAT Reference Circuit ." ELSEVIER Transactions on Microelectronics, 2019.
Yarub Alazzawi, Kenji Aono, Erica L. Scheller , and Shantanu Chakrabartty. "Self-Capacitance based Wireless Power Broadcasting for Internet of Medical Things (IoMT) ." IEEE Transactions on Internet of Things, 2020, under review.
Kondapalli, Sri Harsha, Yarub Alazzawi, and Shantanu Chakrabartty. "Multiaccess in vivo biotelemetry using sonomicrometry and M-scan ultrasound imaging." IEEE Transactions on Biomedical Engineering 65.1 (2018): 149-158.
Kondapalli, Sri Harsha, Yarub Alazzawi, and Shantanu Chakrabartty. "Feasibility of Self-powering and Energy Harvesting using Cardiac Valvular Perturbations." IEEE transactions on biomedical circuits and systems (2018).

## Slide 30: Publications
Conference proceedings
Yarub Alazzawi, Chunqui Qian, and Shantanu Chakrabartty. "Feasibility of non-contact ultrasound generation using implanted metallic surfaces as electromagnetic acoustic transducers." Biomedical Circuits and Systems Conference (BioCAS), 2015 IEEE. IEEE, 2015.
Yarub Alazzawi, and Shantanu Chakrabartty. "Design of CMOS telemetry circuits for in-vivo wireless sonomicrometry." Circuits and Systems (ISCAS), 2016 IEEE International Symposium on. IEEE, 2016.
Yarub Alazzawi, and Shantanu Chakrabartty. "Self-powered system-on-chip for substrate computing and ultrasonic communications." 2017 IEEE 60th International Midwest Symposium on Circuits and Systems (MWSCAS). IEEE, 2017.
Patents
Chakrabartty, Shantanu, Yarub Alazzawi, Srikanth Signamaneni, Keng-Ku Liu, and Mingquan Yuan. "Systems and methods for detecting embedded target elements using signal interference." U.S. Patent Application 16/023,761, filed January 3, 2019.
Chakrabartty, Shantanu, Yarub Alazzawi, Kenji Aono, and Erica L. Scheller “Methods and apparatus for wireless power delivery and remote sensing using self-capacitances” U.S. Patent Application 62/804,470.

## Slide 31: Thank you

## Slide 32: Questions ?