## Slide 1
السيرة العلمية
الاسم :- رشا هاشم مهدي
اللقب العلمي :- مدرس دكتور
مكان العمل :- جامعة النهرين/ كلية الهندسة/ قسم هندسة الليزر والالكترونيات البصرية
التحصيل العلمي:-
شهادة البكالوريوس/ جامعة النهرين/ كلية الهندسة/ قسم هندسة الليزر والالكترونيات البصرية/ 2010
شهادة الماجستير/ جامعة النهرين/ كلية الهندسة/ قسم هندسة الليزر والالكترونيات البصرية/ 2014
شهادة الدكتوراه/ جامعة بغداد/ معهد الليزر للدراسات العليا/ فرع التطبيقات الهندسية والصناعية/ قسم الهندسة الالكترونية والاتصالات/ 2019
الشهادات:-
CCNA - Cisco Certified Network Associate
TOT - Training of Trainers
SPM - Short Project Management
PMP - Project Management Professional
الاهتمامات العلمية:-
Optical Communication
Laser and Medical Applications
Plasmonic Technique
Nano-Technology

## Slide 2: Biomedical Application of Nanoantenna
Dr. Rasha Hashim Mahdi
Oct. 2021

## Slide 3
Introduction
Fabrication
Biomedical Design
Outline

## Slide 4: Nanoparticles (NPs)
Nanoparticles are particles between 1 and 100 nanometers in size. In nanotechnology, a particle is defined as a small object that behaves as a whole unit with respect to its transport and properties.
Introduction

## Slide 5
Optical Nano-Antenna
Metallic optical nano-antennas (also called optical antennas) have optical properties, as high enhancement and subwavelength confinement of the electrical field.
Optical nano-antenna enhance the interaction between light and matter, and hence hold great promise for applications

## Slide 6
Plasmonic Nano-Antenna
As light interact with a metal nano-particle (NP), its conduction electrons driven by the incident electric field in collective oscillations named localized surface plasmon resonances (LSPRs).
LSPRs have an efficient transfer of EM energy from the near to the far-field of metal NPs and vice versa, so it can consider plasmonic nano-structures as nano-antennas, because they operate as same as radio antennas but at higher frequencies.

## Slide 7: Localize Surface Plasmon Resonances (LSPRs)
collective oscillations known as localized surface plasmon resonance

## Slide 8: Nanoantennas
Since LSPRs enable an efficient transfer of EM energy from the near to the far nanoantennas
Gold and Silver
good metallic properties and low absorption.

## Slide 9: Fabrication
A.Thermal Evaporation
B.Colloidal lithography
C.E-Beam lithography
D.Nanoimprint lithography

## Slide 10: Applications
Nano medicine
Solar cell
Fluorescence
Spectroscopy
Raman
spectroscopy

## Slide 11: Nanomedicine (Detect)
Near-infrared fluorescence tomographic images of normal and subcutaneous tumor-bearing mice after injection of a gold NP probe

## Slide 12: Mechanism of Treatment the Tumor
Specifically designed metal NPs into tumor cells
Excitation causes a temperature increase
Plasmonic Structure
Nano-Antenna
Metal+Dielectric
High intensity field
Resonance Frequency
Tumor

## Slide 13
Nanomedicine (remedy)

## Slide 14: Steps of the work

## Slide 15: Steps of the Design
Single design
532 nm
1064 nm
Array
532 nm
1064 nm

## Slide 16: Design of Plasmonic Bow-Tie Optical Nano-Antenna

## Slide 17: Performance of Plasmonic Bow-Tie Optical Nano-Antenna
Fig. The reflectivity of the plasmonic bow-tie optical nano-antenna at the resonance wavelength 532 nm.

## Slide 18: Performance of Plasmonic Bow-Tie Optical Nano-Antenna
Fig. The field distribution in the gap of plasmonic bow-tie optical nano-antenna.

## Slide 19: Design of Array Plasmonic Bow-Tie Optical Nano-Antenna
2×2
4×4
3×3

## Slide 20
NAs array (2×2, 3×3 and 4×4) as a function
of the wavelength for 532 nm.

## Slide 21: Tissue Proposed
Fig. 3D structure of tissue with plasmonic bow-tie optical nano-antenna.
The tissue model consists of tissue in the spherical shapes centered in the front of plasmonic bow-tie optical nano-antenna and surrounding by air.
The tissue with diameter D = 50 nm, 100 nm and 200 nm.

## Slide 22
The tissue with diameter of 100 nm has a specific absorption rate about 5.23 e12 W/Kg
Fig. Side view of point SAR distribution in the tissue of D 100 nm.

## Slide 23: Design of Proposed Tumor

## Slide 24: SAR Calculations

## Slide 25: SAR Calculations
Specific absorption rate as a function of the distance from the tissue at single unit for 532 nm.

## Slide 26: The SAR calculations for (2×2, 3×3 and 4×4) an array nano-antennas at 532 nm
Specific absorption rate as a function of the distance from the tissue at ANs for 532 nm.

## Slide 27
SAR is a measure of electromagnetic power density and subsequent absorption of electromagnetic radiation and conversion to heat by human tissue.
SAR Calculation
SAR = σ|E|2/2ρ (1)
Where:-
σ =conductivity of the tissue-simulating material (Siemens/m)
E = total Root Mean Square (RMS) field strength (Volts/m)
ρ = mass density of tissue-simulating material (kg/m3)
the point specific absorption rate is recommended in this designed. Because the used plasmonic bow-tie optical nano-antenna and tissue in the nano-range, so the mass and the volume could be neglected.

## Slide 28
Temperature Calculation
The relationship between the point SAR and temperature can be established by using the equation of heat (2)
dQ = ρ V C dT (2)
Where:-
Q=the thermal energy (Joule)
V = the volume (m3)
C = the specific heat (J /K. kg)
T= the temperature in Kelvin (K)
Dividing both sides in (2) by (ρ V dt ), and rearranging terms, we can write the following relationship:
(dQ/dt)/ ρ V= C. dT/dt (3)
The left side term of (3), represents the value of the SAR, so it can be used to determine the thermal distribution in tissues for a period of (Δt). It can be written as:
ΔT= (SAR*Δt)/ C (4)

## Slide 29
Time period Calculation
Time period estimation in tumor tissue at single nanoantenna

## Slide 30: Time period in proposed tumor for an array nanoantenna

## Slide 31
The good enhanced field of the plasmonic optical optical nano-antenna is the mean reason to use it in the treatment of diseased tissue.
The optical nano-antenna size is compatible to the corona virus thus it could be used to face COVID19.
The point source of the optical nano-antenna represents the suitable choice to confine the absorbed power in the tissue without affecting the surrounding tissue.
From the extracted results regarding the point SAR is 6.94 e12 W/Kg and the calculated temperature is 64 Co in the tissue.
We can conclude that the designed plasmonic bow-tie optical nano-antenna is an encourage choice in the treatment of the tissue.

## Slide 32
Thanks
for your attention
Dr. Rasha Hashim Mahdi
rashahmahdi@eng.nahrainuniv.edu.iq